## Slide 1: Estimating QoE from QoS in real-time traffic: a Machine Learning approach
Master Degree in
COMMUNICATIONS AND COMPUTER NETWORKS
ENGINEERING
Supervisor: Prof. Martino Trevisan
Co-Supervisors: Prof. Michela Meo
Dena Markudova
Candidate: Ymer Gurra

## Slide 2: Outline
VI
I
Introduction
II
Goals and Objectives
III
Scenario and Methodology
Dataset description
V
Results and Discussion
VI
Conclusions

## Slide 3: Introduction
Video streaming
Quality of Experience (QoE) evaluation
Network Operators / ISP providers:
QoE metrics such as video quality, freezing etc.
Only network level measurements such as:
  Delay
  Jitter
  Throughput etc.

## Slide 4: Goals and Objectives
Mapping QoS parameters into QoE metrics
Test and improve the model’s performance
Build a Machine Learning model

## Slide 5: Thesis Workflow
ONLINE MEETING
Wireshark
App logs
DATA COLLECTION
Statistic producer tool
DATA PRE-PROCESSING
QoS-QoE mapping via ML approach
Performance evaluation
via JITSI
QoS features
QoE features
Classification
Number of samples (1s):
  Total 403 264
  Train 284 243 (70%)
  Test 119 021 (30%)
f-1 score
Mean Absolute Error
WebRTC
50 pcaps (50 GB of data)
Mean
Min
Max
Standard deviation etc.
Regression

## Slide 6: Feature Description
QoS features categories:
a) Interarrival: The time difference between 2 successfully received consecutive packets in a UDP stream
b) Packet length: The size of a packet
c) Interlength: The difference between the lengths of 2 successfully received consecutive packets in a UDP stream.
d) Inter RTP timestamp: Difference between consecutive RTP timestamps
  Packet level statistics:
    Mean
    Standard deviation
    Percentiles
    Skewness
    Kurtossis etc.
QoE metrics (targets):
Resolution : The size in pixels of the received video frames
Smoothness : The number of frames per second perceived at the user side
Concealment : Time spent by the decoder rendering frames that are partially received

## Slide 7: Supervised ML approach
Interarrival (std) | Packet length(kbps) | Interlength (max) | Rtp_int_timestamp (count)
0.002851 | 37.945312 | 9.0 | 50
0.003035 | 38.687500 | 9.0 | 50
0.002728 | 36.945312 | 6.0 | 50
0.004631 | 36.656250 | 26.0 | 50
Resolution (pixels) | Smoothness (fps) | Audio Conceal. | Video Conceal.
320.0 | 30.0 | 0.0 | 0.0
1280.0 | 10.0 | 5.0 | 1.0
240.0 | 9.0 | 2.0 | 0.0
Target-1
Target-2
Target-3
QoS features
Model training
Algorithm
Output (ex.)
Processing
Resolution = 240.0
Smoothness = 3.0
Audio Conceal. = 0.0
Video Conceal. = 1.0
0.00157 | 32.7543 | 5.0 | 50
Test data sample

## Slide 8: Smoothness Prediction
Model | R-squared (R2) | MSE | MAE
Random Forest | 0.87 | 15.02 | 1.43
Decision Tree | 0.84 | 19.0 | 1.64
dataset
Feature selection
Outlier treatment
Anova f-value
Information Gain
Coefficient correlation
Trimming
Flooring and capping
Replacement with median
DATA PRE-PROCESSING

## Slide 9: Resolution Prediction
240 – 480
480 – 960
960 – 1280
> 1280
Model | Precision | Recall | f1-score
Random Forest | 0.93 | 0.90 | 0.91
XG Boost | 0.93 | 0.90 | 0.91
Decision Tree | 0.91 | 0.89 | 0.90
Predicted values
True values

## Slide 10: Concealment Prediction
Model | Precision | Recall | f1-score
Random Forest | 0.80 | 0.61 | 0.64
Decision Tree | 0.60 | 0.60 | 0.60
Audio concealment:
No. of supports
Video concealment:
Model | Precision | Recall | f1-score
Random Forest | 0.58 | 0.59 | 0.59
Decision Tree | 0.59 | 0.61 | 0.60
No. of supports

## Slide 11: Conclusions
Our model is able to predict the following targets:
Smoothness
Resolution
Concealment
Some approaches for concealment improvement:
  Collect more data
  Imbalanced classification techniques: SMOTE, MSMOTE etc.
Observations from a cloud gaming scenario:
  Only one resolution class
  Only one value of smoothness
  Very few concealments
  Different targets need to be defined for this scenario

## Slide 12
Thank you